Midterm Exam, Fall 2003, October 21, 2003

ELEC-4601: Microprocessor Systems

Department of Electronics, Carleton Univesity

Instructor: Maitham Shams                                         Name: ______________________

Aids: All non-speaking allowed 			         ID: ______________________

Duration: 60 minutes					   Mark: ___________ out of 80 ___

[1](8 marks) What happens during a read bus cycle in each of the following states?

- T1: Address is placed on bus;  ALE, DT/R and IO/M activated                  2

- T2: RD signal and DEN activated; READY sampled at the end

- T3: If READY was low, this is a wait state and READY is sampled            2

again in its middle; else no activity (just waiting for data)                     2

- T4: All signals are deactivated to prepare for next cycle                             2

[2](20 marks) Answer the following questions.

- What are the operational modes of an Intel 80386 microprocessor and how do they differ?

- …Real…..... mode: Uses only 1 MB of memory                                           2

- …Protected. mode: Uses all memory                                                           2

- What are functions of IP and FLAG registers?

- IP: Instruction Pointer, holds the address of the next instruction

to be executed.                                                                                       2

- FLAG: Includes bits to control the operation of microprocessor

and bits that show the current status of microprocessor.                  2

- What are the default segment registers for IP and SP? Explain why.

- IP: Code Segment; IP holds address for next instruction in current code                2

- SP: Stack Segment; SP holds address of top of the stack                                        2

- What are the four main control signals in a microprocessor-based system and what are their functions?

- …MRDC :  Memory read control signal                                                       2

- …MWTC:  Memory write control signal                                                       2

- …IORC…: I/O read control signal                                                                2

- …IOWC..:  I/O write control signal                                                               2

[3] (12 marks) Assuming 16-bit Intel instructions translate from machine to assembly code (a) and translate from assembly code to machine (b). Note: if D=1, data flows to REG from R/M and, if D=0, data flows to R/M from REG field.

- 8AF3				1000 10 10 11 110 011

MOV1 DH2, BL2

- MOV  [SI], AH                       1000 10 002 002 1001 1002

8824

[4] (20 marks) In an Intel 80286 processor, the last items stored in the stack are the following hexadecimal values: 75 (very last), FA, 1B, 9E, 12, etc. Assume SS=C300, SP=F200, ECX=30 FD 1C 56, and EAX=A9 7E 42 B8. A “PUSH CX” instruction and a “POP EAX” instruction are executed in that order. Determine the following after executing these instructions.

- ECX: 					30 FD 1C 56			2

- EAX:						FA 75 IC 56			4

- SS:						C300				2

- SP:						F200-2+4=F202		4

- Physical location of the top of stack 	C300*10+F202=D2202	4

- Content of stack (top to bottom):		1B 9E 12 etc. 		4

[5](20 marks) Answer this question assuming that the different parts are completely independent. For each part assume that AX contains 5F9C to start with and determine AX after executing the instruction.

- CMP AX, BX

AX:			0101 1111 1001 1100 	5F9C		2

- NOT AX

AX:			1010 0000 0110 0011	A063		2

- SUB AL, AH

AX:			0101 1111 0011 1101	5F3D		4

- ROR AH, 3

AX:			1110 1011 0011 1101  	EB9C		4

- SAL AL, 4

AX:			1111 0011 1100 0000    	5FC0		4

- MOVSX AX, AL

AX:			1111 1111 1001 1100	FF9C		4