Midterm Exam, Fall 2004, October 20, 2004

ELEC-4601: Microprocessor Systems

Department of Electronics, Carleton University

Instructor: Maitham Shams                                         Name: ____   Solution   ____

Aids: All non-speaking allowed 			         ID: ______________________

Duration: 60 minutes					   Mark: _______50_____ out of 50

[1](8 marks) Using the stack, complete the code to exchange two word-size data items located at DAT1 and DAT2 in the memory.

LEA	AX, DAT1

LEA 	BX, DAT2

PUSH WORD PTR [AX]

PUSH WORD PTR [BX]

POP WORD PTR [AX]

POP WORD PTR [BX]

[2](8 marks) Answer the following questions.

- What is the main difference between a stack segment and a data segment in intel processors?

Stacks grow down in memory and data grows up.

- What are the default segment registers for SI and DI?

- SI: DS		Data Segment

- DI: ES		Extra Segment

- What are the four distinguished ages in computation?

Mechanical, Electrical, Integrated Circuit.

- List two microprocessor specifications that directly affect its performance?

Clock speed, cache size, size of registers, size of data bus.

[3] (4 marks) In Intel 8086 microprocessors, why is the segment register content appended by 0 to generate the physical address?

Segment registers are 16 bits, but the 8086 uses 20-bit addresses. The extra zero is needed to create the physical 20-bit address. Without that one may not create segments in all parts of the memory.

[4] (12 marks) Assuming 32-bit Intel instructions in an 80386. Translate from machine to assembly code (a), and translate from assembly code to machine (b). Note: if D=1, data flows to REG from R/M and, if D=0, data flows to R/M from REG field.

- 89F3	10001001 11110011

opcode for MOV: 100010 , D=0, W=1

MOD=11, therefore reg to reg

REG=110, therefore ESI

R/M=011, therefore EBX

Assembly code: MOV EBX, ESI

- MOV  BX, [SI]

Since it is operating in 32-bit instructions mode, 66 should be appended to switch register sizes to 16 bits instead of 32 bits.	10001011	00011100

Machine Code: 66 8B 1C

[5](10 marks) Write a single intel instruction to replace each of the following.

- DEC	AX			SUB AX, 1

- LEA 	AX, DAT1                  MOV AX, OFFSET DAT1

- NOT	AX			XOR AX, FFFFH

- BT	AX, 5 			TEST AX, 0020H

- MOV	AX, 8 OR 2		MOV AX, 10

[6](8 marks) What are the maximum number of non-overlapping memory segments for an intel 80386 microprocessor (32-bits data bus and 32-bits address bus) operated in the following modes.

a) Real mode

Each segment is 64kB and the total memory is 1MB.

Therefore, 2^20/2^16=16 segments.

b) Protected mode

13-bit selctorss, therefore 2^13 = 8192 descriptors,

but there is a bit (T1), which selects local or global

descriptor tables.

Therefore 8192+8192 = 16384 segments.